DISK I/O issues for the current DIFFEV implementation
The following graph shows the current workflow.
Blue arrows and Names represent I/O that is done just once
this does not need a huge effort
Blue arrows and Names represent I/O that is done over and over again
during the refinement, usually from/to a global disk
DISCUS is run parallel via MPI
Right now this includes a loop over MEMBER x INDIVIDUUM
calculations
Once all of these are finished, KUPLOT reads and merges the INDIVUUM
calculations and writes the current output data into TEMP

---
Current workflow DIFFEV refinements
Definitions
Initialization
Parameters; Summary; GENERATION; Trial_files
Loop over generations
run_mpi DISCUS < dis.diffev.mac > /dev/null
Trial_files
INDI
run_mpi KUPLOT < kup.diffev.mac > /dev/null
INDI
Results
TEMP
compare
Results
Trial_files
Parameters; Summary
backup
FINAL (copy)

---
The main part of disk I/O is the wastefull reading / writing of:
a) Data in INDI
b) Macro text itself
where a) is by far the main problem
2 Solutions have come to my mind:
Quick fix, with moderate efficiency gain
Reduce loops in DIFFEV to MEMBER,
Do indiv loop in DISCUS; write data locally
BIG fix, with complete (?) efficiency gain
Envelope DIFFEV/DISCUS/KUPLOT with a DISCUS_SUITE program
write data locally / into memory only

---
Quick fix, with moderate efficiency gain
Reduce loops in DIFFEV to MEMBER
Move loop over INDIVIDUUM into DISCUS macro and write
Individual data to „/tmp/, that should exist as a local (RAM)Disk
Execute KUPLOT Macro from within the DISCUS macro

---
Quick fix workflow DIFFEV refinements
Definitions
Initialization
Parameters; Summary; GENERATION; Trial_files
Loop over generations
run_mpi DISCUS < dis.diffev.mac > /dev/null
Trial_files
/TMP/INDI
KUPLOT < kup.diffev.mac > /dev/null
/TMP/INDI
Results
TEMP
compare
Results
Trial_files
Parameters; Summary
backup
FINAL (copy)

---
BIG fix, with complete (?) efficiency gain
Envelope DIFFEV/DISCUS/KUPLOT with a DISCUS_SUITE program
write data locally / into memory only
The DISCUS_SUITE program shall have the capability to
Preload macos, including their nested sequence, such that the user
does not feel any difference
Preload macos, including their nested sequence, such that the user
does not feel any difference
Preload general input files required by the macros (automatically ???)
Branch to any of DIFFEV; DISCUS; KUPLOT
Do internal I/O into/from memory for:
global.filename	data accessible by all programs
diffev.filename	data accessible to DIFFEV only
discus.filename	data accessible to DISCUS only
kuplot.filename	data accessible to KUPLOT only
Send (large) data via MPI / openmp from MASTER to SLAVE
and between DIFFEV and DISCUS/KUPLOT

---
Big fix workflow DIFFEV refinements
DISCUS_SUITE
setup
Load all macros including nested code
Store in memory for DISCUS, KUPLOT, ...
diffev
Parameters; Summary; GENERATION
Loop over generations
run_mpi DISCUS for MEMBERS; HYBRID model, one member per node
run_openmp DISCUS within MEMBERS for INDIVIDUUM;
on CPU's of given node
run_mpi KUPLOT for MEMBERS
compare
Parameters; Summary; GENERATION
backup
write best solutions to FINAL

---
MASTER; setup, diffev initialization
MASTER; serial loop over refinement cycles
MPI distributed loop
over members
For individual calculation
for a member openmp(?)
Distributed calculation
For individual calculation
for a member openmp(?)
Distributed calculation
Merge results in KUPLOT
Merge results in KUPLOT
MASTER;	collect KUPLOT results
compare:	derive new trial parameters
backup;	archive best results

---
Big fix workflow DIFFEV refinements
run_mpi DISCUS < dis.diffev.mac > /dev/null
DIFFEV sends GENERATION, Trialfiles, Macros
to slave and on to slave program
Essentially as in the current SOCKET version
Need to ensure that the macros are sent only at
the first call
DISCUS sends the calculated Diffraction pattern back to
DIFFEV via the slave
Might have to change the sequence of loops, make
INDIV the fast loop, and MEMBERS the slow
This would allow DISCUS_SUITE to calculate the
R-value for a specific member and then to free the
memory.
DISK I/O reduced to nothing

---
Big fix workflow DIFFEV refinements
run_mpi KUPLOT < dis.diffev.mac > /dev/null
DIFFEV sends GENERATION, Trialfiles, Macros
and the data for one member
to slave and on to slave program
Essentially as in the current SOCKET version
Need to ensure that the macros are sent only at
the first call
KUPLOT sends the averaged diffraction pattern and
The R-value back toDIFFEV via the slave
DISK I/O reduced to nothing

---
Big fix workflow DIFFEV refinements
compare
DIFFEV updates GENERATION, Parameter and
Summary files
backup
DIFFEV updates current best data files into FINAL
directory, optional by user
DISK I/O reduced to a few files once per cycle i.e. 400 times per refinemennt

---
QUIC fix workflow DIFFEV refinements
Trivial change to be done locally in Erlangen
BIG fix workflow DIFFEV refinements
Urgently needed in Erlangen
Implications to be considered for future PYTHON / SWIFT solutions